CERN –PH/ED

U2F 1.1

USB to FEC Interface Card

User Manual

Authors: H. Boutamine, R. Campagnolo, C. Gonzalez, M. Joos, A. Junique, B. Mota, L. Musa

Created: March 2004

Last Update: 20th May 2005

DRAFT 1.3

# Chapter

1

Functional Description

  - Introduction

The U2F (USB to FEC Interface Card) is an interface card between a PC and the ALICE TPC Front End Card (FEC). For the communication with the PC, the U2F supports the USB 2.0 High Speed (480 Mbit/s) interface. The communication with the FEC is based on the ALTRO protocol as described in the ALTRO Chip User Manual. The bridge between these two interfaces is based on a micro-sequencer that will execute sequentially a set of pre-loaded instructions. In this way the User can send large portions of FEC configuration in an instruction memory and execute the sequence with a single command. These sequences can be composed by ALTRO instructions (micro instructions) and/or higher level macro instructions.

This document contains a description of all accessible registers and memories as well as the macro instructions that can by run by the U2F. At the end of this document, some basic examples of configuration scripts (containing instruction sequences) are proposed. They allow running the system with a minimal set of parameters.

## Architecture

#### 1.2.1 Introduction

The Front End Electronics for the ALICE Time Projection Chamber (TPC) consists of about 560000 channels packed in 128-channel units (Front End Card). Every Front End Card (FEC) incorporates the circuits to amplify, shape, digitize, process and buffer the TPC pad signals. From the control and readout point of view the FECs are organized in 216 partitions, each being an independent system steered by one Readout Control Unit (RCU). The RCU, which is physically part of the on-detector electronics, implements the interface to the Data Acquisition (DAQ), the Trigger and Timing Circuit (TTC) and the Detector Control System (DCS). It broadcasts the trigger and clock information to the FECs, performs the initialization and readout via a high bandwidth bus, and implements monitoring and safety control functions via a dedicated I2C-like link.

Although primarily developed as readout controller for the ALICE TPC FEE, the RCU has been designed to implement control, readout and monitoring functions for any front-end card based on the ALTRO chip. Therefore, while the interface to the front-end units and the core functions are tailored to the ALTRO architecture, the interface to the back-end systems (DAQ, DCS and Trigger) is open to accommodate different technologies and possible upgrades. The resulting architecture and physical layout consist of a board based on a single FPGA, which implements all functions related to the control, configuration, readout and monitoring of the front-end units, on which can be plugged as mezzanine cards the interface boards to the specific back-end systems. In the ALICE case, these two mezzanine cards are the Detector Data Link Source Interface Unit [6] (DDL SIU), which implements a full duplex 200MByte/s optical link and is the ALICE standard interface to the DAQ, and the DCS/Trigger interface card [7], which is also an item common to a number of other ALICE detectors. In particular, the latter incorporates the LHC TTCrx chip [8], through which it receives the clock and trigger information by the TTC system, and implements an intelligent controller and DCS interface based on a FPGA with an embedded processor and an Ethernet Interface.

The U2F card is a variant of the ALICE RCU: it is a single board (does not support any mezzanine card) that incorporates all ALICE RCU functions. However, the interface to the ALICE DAQ and DCS are here replaced by a USB interface, while the interface to the ALICE TTC system is replaced by two LEMO connectors to input external clock and trigger signals.

From the functional point of view the U2F card consists of three main blocks: 1) the ALTRO Bus Controller, which implements all functions related to the communication to the front-end units during the configuration and data readout, and it is described in the section 1.2.2; 2) the Monitoring and Safety Module, which implements the functions described in Section 1.2.3. 3) The USB interface, described in section 1.2.4. It should be noticed that the first two blocks, the ALTRO Bus Controller, and the Monitoring and Safety Module, correspond to the core functions of the ALICE RCU board.

#### 1.2.2 ALTRO Bus Controller

For the initialization and data readout, the communication between the U2F and the FECs is implemented via the ALTRO bus. Physically this is implemented either as PCB-based backplane or with a standard ribbon cable. The ALTRO bus is essentially an extension of the FEC’s internal bus that allows the U2F to access the FEC’s internal components. It is a multi-drop single-master bus, whereas the U2F is the MASTER and the FECs are the SLAVEs. Electrically the bus signals are implemented as GTL lines with the exception of the sampling clock that is transmitted to the FECs as differential PECL.

The ALTRO Bus implements a VME

#### 1.2.3 USB Interface

## Functions

Despite of the name, the U2F card performs key system-level functions: distribution of Trigger and Clock signals to the FECs, configuration of each front-end channel and readout of trigger-related data from the FECs. In parallel the U2F is also responsible for monitoring the voltages, currents, temperature and a number of functional parameters. In case any of the monitored quantities shows an anomalous behaviour, the U2F takes the appropriate action in order to prevent any damage to the FECs or severe system errors. In this section will give a detailed description of the U2F functions.

#### 1.3.1 Trigger and Clock Distribution

The U2F can be operated either with an internal clock, generated by a 40MHz quartz, or with an external clock, which input to the card by means of a LEMO connector. The two sources are exclusive. We will refer to this clock signal as the master clock. Inside the U2F FPGA, from the master clock, starting from the The trigger information and the clock are transmitted to the RCU via the TTCrx chip of the DCS board. The incoming clock (RCLK) and a fixed latency Level-1 trigger pulse, originated in the A-channel of the TTCrx, are broadcasted to all FECs through the ALTRO bus. The sampling clock (SCLK) is derived from the RCLK through a PLL. Its value, which ranges from 5 to 10MHz, is distributed to the FECs via a differential line in order to minimize the noise and, therefore, the signal jitter. The Level-1 trigger word (10 bits) and Level-2 trigger messages (several bytes of information) are received from the TTCrx B-channel.  The Level-1 word and part of the Level-2 message are copied in the event data packet header shipped to the DAQ. The Level-2 message is used to compare the LHC bunch crossing number with the local one, and to generate the Level-2 accept/reject signals for the FECs. Three trigger running modes are possible in the RCU: software trigger mode, used for debugging and calibration purposes; Level-1 mode for detectors using a single-level trigger; and Level-1 + Level-2 mode as in the standard running mode foreseen for the ALICE TPC. In the case of the Level-1 mode, the RCU self generates the Level-2 after the ALTRO acquisition window.

#### 1.3.2 Configuration of the FECs

The configuration parameters for the FECs are stored in the U2F Instruction Memory. A sequencer fetches these instructions, decodes their content and executes them in the form of a single ALTRO instruction (RCU micro instruction) or sequence of them (RCU macro-instruction). The macro instructions allow, for example, to write or to verify the full content (or part of it) of a given ALTRO pedestal memory. Another example is a RCU macro that handles a complete trigger sequence to exercise the readout chain.

#### 1.3.3 Data Readout

The readout of one event is performed in two separate phases, which are consecutive for a given event, but can otherwise be activated concurrently. In a first phase the trigger information is received by the U2F and broadcast to all FECs in the system, starting the digitisation of each channel, which lasts for a programmable amount of time (see TRCFG register in ALTRO User Manual). During this phase data processing takes place in the ALTROs. In the second phase, information is moved by the U2F from the ALTRO’s multi-event buffer into the internal data memory first and then into the PC, on a channel-by-channel basis. The U2F data memory consists of two banks, working in interleaved mode, each being able to store the event data of one single ALTRO channel. While data from one bank is being pushed into the USB channel, data from the next ALTRO channel is stored into the other one. The time needed to complete the readout depends on the size of the event, but other triggers can be processed during the readout of the previous event, as long as the multi-event buffers in the FEC are not full. Dead time can be generated only when this condition occurs. FECs containing valid data are enabled to assert data on the bus by individual addressing, according to an Active Channel List stored in the U2F.

#### 1.3.4 Data Format

In Data Pushed mode, the ALTRO data blocks are shipped by the U2F card to the PC with the following format:

Assuming a data block of 4*M words,

ALTRO_Data[N] 	= U2F_Data[N][9:0];

ALTRO_Data[N+1] 	= (U2F_Data[N][15:10] & 0x03f) | (U2F_Data[N+1][3:0] << 6)& 0x3C0);

ALTRO_Data[N+2]	= U2F_Data[N+2][9:0];

ALTRO_Data[N+3] 	= (U2F_Data[N+2][15:10] & 0x03f) | (U2F_Data[N+3][3:0] << 6)& 0x3C0);

for N = 1,2,3, ..., 4*(M-1), and

ALTRO_ADDRESS = U2F_Data[M][11:0]

ALTRO_BLOCK_LENGTH = U2F_Data[M+1][20:16] & 0x00f) | (U2F_Data[M+2][5:0] << 4)& 0x3C0);

# Chapter

2

Mode of Use and Operation

USB Interface

#### Data Transport Format

The communication between the PC (host) and the U2F card (device) is done via structured data blocks (Messages) that are written/read to/from the Endpoint 6(2) in High-Speed Bulk Mode.

IMPORTANT

The Endpoint 6 and 2 have a capacity of 1 Kbytes, which in the actual version of the U2F card, defines the maximum size of the data block transferred to/from the device. However, it is foreseen an upgrade that will remove any limitation in the size of the data blocks exchanged between host and device.

The format of the Message is defined in table 1.1.

|  | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | Block Length (11 bits) (1) | Operation Code (5 bits) (2) ) |
| 1 | Address (16 bits) (3) |
| 2 | Data 0 (16 bits) (4) |
| ….. |
| N + 111 | Data N-1 (16 bits) |

Table 1.1. Message format

Hereafter follows a description of the fields that compose the Message.

(1) Operation Code (5 bits)

It specifies the message typology. The present version supports only two types of Message (table 1.2), the Write Instruction and the Read Instruction. In the case of a Read Instruction, the Message consists of 2 words. For a Write Instruction, the Message consists of N+2 words, N being the number of data words to be written in the destination unit defined by the address field of the Message.

| Instruction Name | Code | Description |
| --- | --- | --- |
| Write | 0x00 | Write a data block with the specified Length at the specified Address |
| Read | 0x01 | Read a data block with the specified Length from the specified Address |

Table 1.2. Instruction set

(2) Block Length (11 bits)

It specifies the number of 32-bit data words to be transferred in a Write/Read Instruction.

(3) Address (16 bits)

It specifies the address of the destination unit inside the U2F card in a Write/Read Instruction. The U2F address space is defined in the tables 2.1 (Memories), 2.2 (Registers) and 2.3 (Commands).

(4) Data (16 bits)

Data to be written at specified Address in a Write Instruction. Two consecutive Data words form the 16 LSB and 16 MSB, respectively, of the 32-bit word that will be written at the specified Address. Since Block Length is expressed in terms of 32-bit words, the number of Data words must be equal to 2 x Block Length and is, therefore, even.

Storage Elements (Memories and Registers)

The U2F interface card contains a set of Configuration and Status Registers (CSR) and a set of Data and Instruction Memories, which are mapped in a 16-bit address space as defined in tables 2.1 and 2.2.

| Name | Size | Base Address and Access | Description |
| --- | --- | --- | --- |
| Instruction Memory (IMEM) | 24bit x 256 | 0x7000 R/W | It contains the Instruction Sequence to be executed either in configuration or readout. |
| Pattern Memory (PMEM) | 10bit x 1024 | 0x6800 R/W | Contains Pedestal values to be sent or compared. |
| Result Memory (RMEM) | 20bit x 128 | 0x6000 R/W | The result of each ALTRO READ instruction is stored in this memory. |
| Active Channel List (ACL) | 16bit x 256 | 0x6400 R/W | It contains the list, in a per channel basis, of all the channels that will be readout. Each line corresponds to an ALTRO, and each bit to a channel. |
| Data Mem 1 – Low (DML1) | 20bit x 256 | 0x7400 R | Low 20bit of data MEM 1 |
| Data Mem 1 – High (DMH1) | 20bit x 256 | 0x7500 R | High 20bit of data MEM 1 |
| Data Mem 2 – Low (DML2) | 20bit x 256 | 0x7C00 R | Low 20bit of data MEM 2 |
| Data Mem 2 – High (DMH2) | 20bit x 256 | 0x7D00 R | High 20bit of data MEM 2 |

Table 2.1: U2F Addressable Memories

| Name | Access | Size | Base Address | Description |
| --- | --- | --- | --- | --- |
| ERRST | R | 4bit | 0x7800 | It contains the status and error information. |
| TRCFG1 | R/W | 29bit | 0x7801 | It contains the Trigger configuration and Trigger Status. |
| TRCNT | R | 32bit | 0x7802 | It contains the counters of L1 triggers received and L1 triggers accepted. |
| LWADD | R | 16bit | 0x7803 | It contains two 8bit words with the location of the last written words in each one of the memory banks |
| IRADD | R | 20bit | 0x7804 | It contains the address of the last instruction sent to the ALTROs. |
| IRDAT | R | 20bit | 0x7805 | It contains the data of the last instruction sent to the ALTROs. |
| EVWORD | R | 5bit | 0x7806 | It contains information on the dataflow related to the last trigger |
| ACTFEC | R/W | 16bit | 0x7807 | It controls the power state of each FEC connected to the ALTRO bus. |
| FMIREG | R/W | 16bit | 0x7808 | Input register to write into the FEC’s flash memory. FMIREG[15:8] contains the 8-bit address of the Flash Memory, FMIREG[7:0] contains the 8-bit data. |
| FMOREG | R/W | 8bit | 0x7809 | Register containing the results of the last Flash Memory Read instruction. |
| TRCFG2 | R/W | 2bit | 0x780A | It controls the readout mode, TRCFG2[0], and the Hardware Trigger, TRCFG2[1]. If TRCFG2[0] is set to 1 (defaults to 0), the data-pushed mode is enabled. If TRCFG2[1] (defaults to 0), the Hardware Trigger is enabled. |

Table 2.2: Configuration and Status Registers (CSRs) Table

It should be noticed that independently of whether the width of the addressed storage element exceed or not 16 bits, each data word is beard in the Message by two consecutive Data word. When addressing IMEM at the location 0x7000, for example, we have:

- IMEM[15:0]   = Message[2][15:0]

- IMEM[23:16] = Message[3][7:0]

For PMEM at 0x6800:

- PMEM[9:0] @ 0x6800 = Message[2][9:0]

- PMEM[9:0] @ 0x6801 = Message[4][9:0]

It follows a detailed description of the Configuration and Status Registers.

ERRST-

Error and Status register

| Instruction Code | 7800 h |
| --- | --- |
| Width | 5 |
| Register Type | Status |
| Access Type | Read |

Instruction Coding

| 31 5 | 4 | 3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- |
| X | HWADD ERROR | ALTRO ERROR | TIMEOUT | ABORT | PATTERN ERROR |

Description

| Parameter | Description | Range |
| --- | --- | --- |
| PATTERN ERROR | This bit is set to “1” if there is a mismatch in the comparison of the PMREAD U2F instruction | 0 – 1 |
| ABORT | It signals that the instruction sequence has been aborted | 0 – 1 |
| TIMEOUT | This bit is set to “1” if the front-end cards do not respond within 32 clock cycles | 0 -- 1 |
| ALTRO ERROR | This bit corresponds to the errorb line of the ALTRO bus | 0 -- 1 |
| HWADD ERROR | This bits signals a mismatch between the channel address contained in the data of a readout and the channel address requested in that readout | 0 -- 1 |

TRCFG1-

Trigger Configuration Register I

| Instruction Code | 7801 h |
| --- | --- |
| Width | 29 |
| Register Type | Config /Status |
| Access Type | Read / Write |

Instruction Coding

| 31 29 | 28 26 | 25 | 24 | 23 20 | 19 | 18 | 17 | 16 15 | 14 | 13 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| WRPT | RDPT | FULL | EMPTY | REMB | X | POP | OPT | MODE | BMD | TW |

Write Access

Description

| Parameter | Description | Range |
| --- | --- | --- |
| TW | This register contains the number of clock cycles that the system waits after the arrival of the L1 trigger and the issuing of the L2 trigger. Only usable in trigger mode = 2 | 0 – 3FFF |
| BMD | Buffer Mode: “0” for 4 buffers and “1” for 8 buffers | 0 – 1 |
| MODE | Trigger Mode: for the U2F application should be set to 2 | 0 -- 3 |
| OPT(*) | This bit enables the readout optimization using the board controller | 0 – 1 |
| POP | This bit enables a popped readout scheme controlled by an external master e.g. USB or DCS | 0 – 1 |
| REMB | Remaining free buffers in the multi-event buffer | 0 -- F |
| EMPTY | Signals that the multi-event buffer has no events to be readout | 0 – 1 |
| FULL | Signals that the multi-event buffer is full and cannot accept any events | 0 – 1 |
| RDPT | Read pointer position | 0 – 8 |
| WRPT | Write pointer position | 0 – 8 |

(*) Not yet implemented

TRCNT-

Trigger Counter

| Instruction Code | 7802 h |
| --- | --- |
| Width | 32 |
| Register Type | Status |
| Access Type | Read |

Instruction Coding

| 31 16 | 15 0 |
| --- | --- |
| Number of L1 triggers Received | Number of L1 triggers Accepted |

Description

| Parameter | Description | Range |
| --- | --- | --- |
| NTR | Number of L1 triggers Received. | 0 – FFFF |
| NTA | Number of L1 triggers Accepted | 0 – FFFF |

LWADD-

Last Written address in the Memory banks

| Instruction Code | 7803 h |
| --- | --- |
| Width | 16 |
| Register Type | Status |
| Access Type | Read |

Instruction Coding

| 31 16 | 15 8 7 0 |
| --- | --- |
| X | Address of the last memory location written in bank 2 | Address of the last memory location written in bank 1 |

IRADD-

Address of last ALTRO Instruction

| Instruction Code | 7804 h |
| --- | --- |
| Width | 20 |
| Register Type | Status |
| Access Type | Read |

Instruction Coding

| 31 20 | 19 0 |
| --- | --- |
| X | Address of the last ALTRO instruction sent |

IRDTA-

Data of last ALTRO Instruction

| Instruction Code | 7805 h |
| --- | --- |
| Width | 20 |
| Register Type | Status |
| Access Type | Read |

Instruction Coding

| 31 20 | 19 0 |
| --- | --- |
| X | Data of the last ALTRO instruction sent |

EVWORD-

Event Word

| Instruction Code | 7806 h |
| --- | --- |
| Width | 5 |
| Register Type | Config /Status |
| Access Type | Read Only |

Instruction Coding

| 31 |  |  | 5 | 4 | 3 | 2 | 1 | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| X | Trigger | Start Event | End Event | DMEM2 FLAG | DMEM1 FLAG |

Description

| Parameter | Description | Range |
| --- | --- | --- |
| DMEM1 FLAG | This register is set to 1 when data of one ALTRO channel has been written into DMEM1. | 0 – 1 |
| DMEM2 FLAG | This register is set to 1 when data of one ALTRO channel has been written into DMEM1. | 0 – 1 |
| End Event | This bit is set to 1 when the U2F card has accomplished the readout of one complete event. This occurs when data from the last ALTRO channel, according to the ACL , has been completely transferred in DMEM. | 0 – 1 |
| Start Event | This bit is set to 1 when the U2F card starts executing the data readout. | 0 – 1 |
| Trigger | Signals that a trigger has been received. When set to 1, it will prevent the U2F to process any further trigger. | 0 – 1 |

ACTFEC-

Active Front End Cards

| Instruction Code | 7807 h |
| --- | --- |
| Width | 16 |
| Register Type | Config /Status |
| Access Type | Read/Write |

Instruction Coding

| 31 |  |  | 16 | 15 |  |  |  | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| X | ACTFEC |

Description

Each bit controls the power switch of the card with the corresponding address. For Example, if ACTFEC[15:0] = 0x0005, the FECs with address 0 and 4 are ON, while all other FECs are OFF.

FMIREG-

Flash Memory Input Register

| Instruction Code | 7808 h |
| --- | --- |
| Width | 16 |
| Register Type | Config /Status |
| Access Type | Read/Write |

Instruction Coding

| 31 |  |  | 16 |
| --- | --- | --- | --- |
| X | FM Address | FM Data |

Description

Flash Memory Input Register.  It stores the Address and Data of the next Flash memory Write Instruction. The slash memory

FMOREG-

Flash Memory Ouput Register

| Instruction Code | 7809 h |
| --- | --- |
| Width | 8 |
| Register Type | Config /Status |
| Access Type | Read/Write |

Instruction Coding

| 31 |  |  | 8 |
| --- | --- | --- | --- |
| X | FM Data |

Description

Flash Memory Output Register.  It stores the result of the last Flash memory Read Instruction.

TRGCFG2-

Trigger Configuration Register I

| Instruction Code | 780A h |
| --- | --- |
| Width | 2 |
| Register Type | Configuration |
| Access Type | Read/Write |

Instruction Coding

| 31 |  |  | 2 1 0 |
| --- | --- | --- | --- |
| X | Hardware Trigger Enable | Readout Mode |

Description

Hardware Trigger Enable enables the Hardware Trigger which is input to the board via the TRIGG_IN input (LEMO connector PX1). Readout Mode defined the readout scheme. When Readout Mode is set to 0, for each ALTRO channel, the PC has to read the EVWORD register, execute the readout of the Data Memory and reset the corresponding EVWORD bit. If Readout Mode is set to 1, the U2F card will keep pushing trigger related data into the USB channel (one USB packet per channel).

U2F Commands

Besides the Write and Read Instructions to a storage element, the U2F card supports a set of 10 Commands (table 2.3). The Commands, which belong to the category of Write Instructions, will be executed by a Finite State Machine.

| Name | Base Address | Description |
| --- | --- | --- |
| RS_STATUS | 0x6C01 | It resets the ERRST (status) register |
| RS_TRCFG | 0x6C02 | It resets the TRCFG (trigger configuration) register |
| RS_TRCNT | 0x6C03 | It resets the TRCNT (trigger counter) register |
| EXEC | 0x00XX | Starts the execution of a sequence in the instruction memory at the address specified in XX (8bits) |
| ABORT | 0x0800 | Aborts any sequence taking place on the instruction memory |
| FECRST | 0x2001 | Executes a Global Reset of all FECs |
| SWTRG | 0xD000 | Software Trigger |
| RS_DMEM1 | 0xD001 | Resets the DMEM1 Flag in the EVWORD Register |
| RS_DMEM2 | 0xD002 | Resets the DMEM2 Flag in the EVWORD Register |
| TRG_CLR | 0xD003 | Resets the EVWORD Register |
| WRFM | 0xD004 | Write FEC’s Flash Memory |
| RDFM | 0xD005 | Read FEC’s Flash memory |

Table 2.3: Commands Summary Table

Instruction Sequence Code

The U2F instructions are coded in 24bit and can be divided into RCU-specific commands and ALTRO Instructions. In both cases the basic structure of each instruction is:

| 22 | 21 | 20 | 19 16 | 15 0 |
| --- | --- | --- | --- | --- |
| U2F/ ALTRO | R/W | Position | U2F Instruction Code | U2F Instruction Data |
|  |  |  | ALTRO Instruction Format |

Table 2.6: 40-bit bi-directional Address/Data bus

U2F/ALTRO. It contains information on the type of instruction. This bit is set to “1” it is an ALTRO instruction and “0” for an U2F command.

R/W. This bit is set to “1” for a WRITE instruction or command and to “0” for READ access.

Position. This bit indicates if the current instruction is the first half or second half of an ALTRO instruction. Since the ALTRO bus is 40bit, two U2F instructions are required to form a single ALTRO instruction. In the case of ALTRO commands or READ instructions (20bit) the first U2F instruction is not required. The POSITION bit is set to “0” for the first half of an ALTRO instruction; otherwise it is set to “1”.

RCU Instruction Code. This 4bit register contains the code of the specific U2F command.

RCU Instruction Data. This 16bit register contains meaningful data related with specific U2F command. In some cases this field is not needed.

ALTRO Instruction Format. This 20bit field contains either the first or second part of an ALTRO instruction [ALTRO User’s Manual].

Table 2.7 shows a summary of the existing macro-instructions which are U2F specific. To note that on top of those, all the ALTRO commands and register accesses are possible. In this sense a given instruction sequence can contain a mix of ALTRO-specific commands and U2F macros. A more detailed explanation on each instruction is given subsequently.

Instruction Set: Summary Table

| Name | Base Address | Description |
| --- | --- | --- |
| JUMP | 0x0 | Jump or Loop Instruction. |
| RS_STATUS | 0x1 | This instruction sends a reset to the ERRST register. |
| RS_TRCFG | 0x2 | This instruction sends a reset to the TRCFG register. |
| RS_TRCNT | 0x3 | This instruction sends a reset to the TRCNT register. |
| CHRDO | 0x6 | This instruction sends the ALTRO CHRDO command to all the channels whose front-end card is active (cf. Active Front-end card List) and whose corresponding bit in the Active Channel List (ACL) is set to “1”. |
| PMREAD | 0x7 | This instruction sends the ALTRO PMADD (W) and PMDTA (R) commands to the channel with address CHANNEL ADDRESS and to all possible 1024 locations of the corresponding ALTRO pedestal memory. The result is compared with the content of the Pattern memory of the RCU. Any error in the comparison sets the bit[0] of the ERRST status register to “1”. |
| PMWRITE | 0x8 | This instruction sends the ALTRO PMADD (W) and PMDTA (W) commands to the channel with address CHANNEL ADDRESS to all 1024 locations of the corresponding ALTRO pedestal memory. The instruction is broadcasted to all channels if the bcast bit is set to “1”. |
| END | 0x9 | This instruction signals the end of the instruction sequence. It is mandatory to this instruction in order to avoid leaving the system in a busy state permanently. No more instructions will be executed after the END instruction is called. |
| WAIT | 0xA | The WAIT instruction forces the instruction pointer to remain in the current position for a number of clock cycles defined by Ncycles. |
| TRIGGER | 0xB | The TRIGGER instruction forces the instruction pointer to remain in the current position until a hardware L1 trigger reaches the U2F. |

Table 2.7: Instruction Table

| Instruction Code | 0 h |
| --- | --- |

-JUMP-

Jump or Loop Instruction

Instruction Coding

| 22 20 | 19 16 | 15 | 14 8 | 7 0 |
| --- | --- | --- | --- | --- |
| 3 | 0 | JnL | N | ADDRESS |

| Parameter | Description | Range |
| --- | --- | --- |
| JnL | JUMP not LOOP | 0 – 1 |
| N | Number of Loops before continue | 0 – 7F |
| ADDRESS | Address to which the instruction sequence pointer will jump | 0 -- FF |

Description

This instruction allows the instruction sequence pointer to jump into a user defined location in the instruction memory.  There are two possible modes: JUMP mode and LOOP mode. In Jump mode, the bit JnL is set to “0”, the sequence pointer is directed to the location given by ADDRESS with no other conditions. In LOOP mode, the bit JnL is set to “1”, the sequence pointer will be directed to ADDRESS only if the current instruction has been called a number of times less or equal to N. When this number is reached, the sequence continues and does not jump.

Example

The following instruction sequence will loop 10 times on instruction 0x0005 and 0x0006, before continuing to instruction 0x0008.

Instruction Address				Instruction Code

0x0005					XXXXXX

0x0006					XXXXXX

0x0007					0x308A05

0x0008					XXXXXX

-RS_STATUS-

| Instruction Code | 1 h |
| --- | --- |

Reset Status Register Instruction

Instruction Coding

| 22 20 | 19 16 | 15 0 |
| --- | --- | --- |
| 3 | 1 | X |

Description

This instruction sends a reset to the ERRST register.

-RS_TRCFG-

| Instruction Code | 2 h |
| --- | --- |

Reset Trigger Configuration Register

Instruction Coding

| 22 20 | 19 16 | 15 0 |
| --- | --- | --- |
| 3 | 2 | X |

Description

This instruction sends a reset to the TRCFG register.

-RS_TRCNT-

| Instruction Code | 3 h |
| --- | --- |

Reset Trigger Counter Instruction

Instruction Coding

| 22 20 | 19 16 | 15 0 |
| --- | --- | --- |
| 3 | 3 | X |

Description

This instruction sends a reset to the TRCNT register.

-CHRDO-

| Instruction Code | 6 h |
| --- | --- |

Send Channel Readout Instruction

Instruction Coding

| 22 20 | 19 16 | 15 0 |
| --- | --- | --- |
| 3 | 6 | X |

Description

This instruction sends the ALTRO CHRDO command to all the channels whose front-end card is active (cf. Active Front-end card List) and whose corresponding bit in the Active Channel List (ACL) is set to “1”.

-PMREAD-

| Instruction Code | 7 h |
| --- | --- |

Pedestal Read Instruction

Instruction Coding

| 22 20 | 19 16 | 15 12 | 11 0 |
| --- | --- | --- | --- |
| 3 | 7 | X | CHANNEL ADDRESS |

Description

This instruction sends the ALTRO PMADD (W) and PMDTA (R) commands to the channel with address CHANNEL ADDRESS and to all possible 1024 locations of the corresponding ALTRO pedestal memory. The result is compared with the content of the Pattern memory of the U2F. Any error in the comparison sets the bit[0] of the ERRST status register to “1”.

PMWRITE-

| Instruction Code | 8 h |
| --- | --- |

Pedestal Write Instruction

Instruction Coding

| 22 20 | 19 16 | 15 13 | 12 | 11 0 |
| --- | --- | --- | --- | --- |
| 3 | 8 | X | bcast | CHANNEL ADDRESS |

| Parameter | Description | Range |
| --- | --- | --- |
| bcast | The instructions is broadcasted to all channels | 0 – 1 |
| CHANNEL ADDRESS | Channel Address to which the Pedestal Memory Write is sent | 0 -- FFF |

Description

This instruction sends the ALTRO PMADD (W) and PMDTA (W) commands to the channel with address CHANNEL ADDRESS to all 1024 locations of the corresponding ALTRO pedestal memory. The instruction is broadcasted to all channels if the bcast bit is set to “1”.

END

| Instruction Code | 9 h |
| --- | --- |

End Instruction

Instruction Coding

| 22 20 | 19 16 | 15 0 |
| --- | --- | --- |
| 3 | 9 | X |

Description

This instruction signals the end of the instruction sequence. It is mandatory to this instruction in order to avoid leaving the system in a busy state permanentely. No more instructions will be executed after the END instruction is called.

WAIT-

| Instruction Code | A h |
| --- | --- |

Wait Instruction

Instruction Coding

| 22 20 | 19 16 | 15 0 |
| --- | --- | --- |
| 3 | A | Ncycles |

Description

The WAIT instruction forces the instruction pointer to remain in the current position for a number of clock cycles defined by Ncycles.

TRIGGER-

| Instruction Code | B h |
| --- | --- |

Trigger Instruction

Instruction Coding

| 22 20 | 19 16 | 15 0 |
| --- | --- | --- |
| 3 | B | X |

Description

The TRIGGER instruction generates a hardware trigger (L1) that will be seen and treated as an external signal. The combination of this instruction with the WAIT and LOOP instructions can provide a programmable in-circuit arbitrary trigger generator.

Example

The following instruction sequence will generate 10 L1 triggers spaced by 128 times the RCU clock period, typically 25ns.

Instruction Address				Instruction Code

0x0000					0x3B0000

0x0001					0x3A00FF

0x0002					0x308A00

0x0003					0x390000